## Slide 1: Hidden Moving Target Defense in Smart Grids
Jue Tian1,2 Rui Tan2 Xiaohong Guan1,3 Ting Liu1,4
1. Xi’an Jiaotong University, P.R. China
2. Nanyang Technological University, Singapore
3. Tsinghua University, P.R. China
4. Cornell University, U.S.

## Slide 2: Motivation
59% attacks on critical infrastructures target grid [US DHS’13]
  Night Dragon: grid data exfiltration [McAfee’11]
  Dragonfly: Trojan horses in grid control systems [Symantec’14]
  BlackEnergy Trojan shut down 1.4 million people’s power supply in Ukraine [WeLiveSecurity’15]

## Slide 3: State Estimation
DC State estimation
  Input: line flow z
  Output: voltage phase estimation
Bad data detection (BDD)
Bad data exists!
Measured data
Estimated data
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 4: Moving Target Defense
False data injection
  Corrupt measurements
  Bypass BDD [Liu CCS’09]
Moving target defense (MTD)
  Lines are equipped with distributed flexible ac transmission system (D-FACTS) devices
  Actively perturbs line susceptances [Rahman MTD’14]
DETECTED!
Attack vector
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 5: Outline
Motivation and background
Problem statement
Construction and properties of hidden MTD
Simulations
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 6: More Intelligent Attacker
Detect the activation of MTD using BDD
  MTD activation detection drives the attacker to obtain new H Risk is not substantially reduced
OK!
Launch the attack
MTD has been activated
Cancel the original attack plan
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 7: Example
Arbitrary MTD is not stealthy to attacker
  Existing method [Rahman MTD’14]
arbitrary
Case |  |  |  |  |  |  | 
Original |  |  |  | -107.3 | -24.7 | 62.7 | 0
After MTD | -1.98 | 0 | 0 | -110.2 | -21.8 | 59.8 | 5.1
D
Table: Arbitrary MTD approach.
Not stealthy!
Figure: 3-bus system.
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 8: Hidden MTD
New MTD strategies
  Hidden MTD:
  Stealthy to attacker
  Power flow invariant MTD (PFI-MTD)
  Power flows remain unchanged after MTD
Research questions
  Equivalence btw hidden and PFI?
  How to construct hidden MTD?
  Existence condition of hidden MTD?
Hidden MTD
PFI-MTD
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 9: Outline
Motivation and background
Problem statement
Construction and properties of hidden MTD
Simulations
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 10: Equivalence btw Hidden and PFI (1)
Condition for PFI-MTD
Lemma：An MTD H’ is a PFI-MTD if and only if there exists x’’, such that Hx = H’x’’.
Case |  |  |  |  |  |  |  |  | 
Original |  |  |  | -107.3 | -24.7 | 62.7 | -3.10 | -0.81 | 0
After PFI-MTD | -1.04 | 0.83 | -1.47 | -107.3 | -24.7 | 62.7 | -2.94 | -0.85 | 0
Table: PFI-MTD approach.
Figure: 3-bus system.
D
D
D
Stealthy!
Intuition: MTD
Only if PFI-MTD
If H’ has full column-rank, then x’’ is unique.
From ,
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 11: Equivalence btw Hidden and PFI (2)
Proposition：An MTD is a hidden MTD if and only if it is a PFI-MTD.
Hidden MTD
PFI-MTD
Intuition of Hidden MTD  PFI-MTD
MTD:
Hidden MTD: ( can bypass BDD based on H)
From Lemma, hidden MTD H’ is PFI-MTD.
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 12: Construction of Hidden MTD
Choose the system state after MTD x’’
Directly calculate H’
Compute the H’ according to
Difficult!
Lemma：An MTD H’ is a PFI-MTD if and only if there exists x’’, such that Hx = H’x’’.
H’ is a Huge matrix!
For 118-bus system,
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 13: Existence of Hidden MTD
If and only if
  : immutable part of H
  Only related to D-FACTS deployment
D
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 14: Existence of Hidden MTD
If and only if
  : immutable part of H
  Only related to D-FACTS deployment
D
D
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 15: Hidden MTD Construction Algorithm
Existence condition
Construct new H’
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 16: Outline
Motivation and background
Problem statement
Construction and properties of hidden MTD
Simulations
Notes: State estimation is used in system monitoring to best estimate the power grid state
through analysis of meter measurement data and power system models.
In POWER GRID, state estimation means estimating State Variables from the Meter Measurements.
The meter measurements may include bus voltages, bus real and reactive power injections, and branch reactive power flows in every subsystem of a power grid.
The state variables include all the bus voltages and the angles of bus voltages. If the number of buses is n, then the number of state variables if 2*n-1.
Usually the number of Meter Measurement is much more than that of state variables.
The whole power grid can be modeled as AC power flow model or DC power flow model.

## Slide 17: Simulation Setting
Matlab & Matpower Toolbox
IEEE 14-bus system
All lines are D-FACTS equipped
Measurement noise and threshold
  Noiseless: threshold
  Noisy:
Figure: 14-bus system
with false alarm rate 5%.

## Slide 18: MTD Stealthiness
Magnitude of MTD: q
  Adjusting capability of line susceptance
  General setting: 20%; Low load condition: much larger (e.g., 90%)
Notes: PFI-MTD is always stealthy when noiseless.
Noise slightly reduce MTD’s stealthy.
Arbitrary MTD is not stealthy.

## Slide 19: Attack Detection Probability
Attacker is able to corrupt measurements of all sensors
FDI attack with small magnitude

## Slide 20: Conclusion
MTD under a more adversary setting
  Attacker can detect the activation of arbitrary MTD
Hidden MTD
  Equivalence to power flow invariant MTD
  Construction algorithm
  Existence condition
Ongoing work
  Hidden MTD under ac power flow model
  Hidden MTD’s completeness